## Slide 1: MotoButtons 2 User’s Guide
September 27, 2024

## Slide 2: Device Overview
Color (RGB) mode, action and state indicator LED
4-way or 5-way (center button) joystick
A
B
C
LED Interpretation
5V DC power (from USB cable)
Color | Meaning
Red | 1. Initial power on 2. Virtual button activated 3. (Flashing) Controller orientation changed at power on
White | Power on completed Keypress (optional)
Blue | Solid: Bluetooth enabled Flashing: Bluetooth searching for connection
Green | Mouse mode
Yellow | DMD2 Mode
Cyan | MyRouteApp mode
Magenta | Media player mode
Long press “C” to activate additional “virtual button”
All buttons (except joystick directional input) activate when released, not when pressed!

## Slide 3: Changing the Installation Orientation
Depending on how you choose to install the unit, you may need to set the orientation of the device. This way, “up” on the joystick will be “up” on your phone or tablet.
Setting the orientation
Hold the joystick UP before applying power. Release once the LED flashes RED.
The setting will be stored for future power cycles.

## Slide 4: Changing the Mode
You can change the mode at any time by long pressing two buttons.
Changing the mode
Holding both the A and B buttons for 1 second. When the mode changes, the LED will cycle to the next color.
The device remembers the mode during power cycles.
A
B
C
Hold both buttons (A and B) for 1 second
MyRouteApp
DMD2
Mouse
Media Player

## Slide 5: Activating the Virtual Button (4-way joysticks)
To accommodate controllers with only a 4-way joystick (no center press), button C can be held down (long press) to simulate the center click of the joystick.
Virtual joystick center press
Hold down Button C for 1 second. The LED will turn RED, then release the button.
A
B
C
Hold “C” down for 1 second to simulate joystick center press

## Slide 6: Mouse Mode
Joystick Hold up, down, left, right to move cursor. Press center for mouse or finger press (5-way only). Holding longer than half a second moves cursor rapidly.
Button C Mouse or finger press (necessary for 4-way joysticks).
A
B
C
Move pointer
Press for finger tap (click)

## Slide 7: DMD2 Mode
Joystick Press for enter or change direction/page.
Button A F6 key
Button B F7 key
Button C Enter Long press: F5 key
A
B
C
Direction/ page
Enter
Enter (F5 long press)
F6
F7

## Slide 8: Media Player Mode
Joystick Up/down: increase/decrease music volume Left/right: previous/next track Center press: mute music
Button A Play or pause music
Button B Stop music
Button C Increase display brightness Long press: Mute music
A
B
C
Mute
Increase brightness (mute long press)
Stop music
Play or pause music
Change track
Adjust volume

## Slide 9: MyRouteApp Mode
Joystick Pan map or change field. Center press: operate compass
Button A Zoom in
Button B Zoom out
Button C Open menu Long press: start navigation
A
B
C
Direction/ pan map
Operate compass
Enter (start navigation long press)
Zoom in
Zoom out

## Slide 10: Reprogramming the Firmware
Due to a bug in the Seeed XIAO microcontroller (MCU), a special button combination is necessary to put the MCU in firmware upload mode. This is known as “DFU” mode.
Entering DFU mode
Connect the USB-C port on the MCU to a computer.
Simultaneously hold down buttons A and B for 10 seconds until the LED goes out.
The MCU enters DFU mode. Select the other / new COM (serial) port in the Arduino IDE and click the upload firmware button.
A
B
C
Hold buttons A and B for 10 seconds (until LED goes out)
2. Select the other COM port for firmware upload
3. Click upload button

## Slide 11: Issues, Suggestions or Questions?
If you encounter issues, have suggestions or other questions, please submit an “issue” in the GitHub repository page. https://github.com/joncox123/MotoButtons2/issues
Alternatively, you may ask the community for help on the ADV Rider forum. However, bugs or issues must be submitted to the GitHub issue tracker.
ADV Rider MotoButtons Forum
Unfortunately, the author cannot respond directly to e-mails.